Part A:

The path of ftrace
/sys/kernel/debug/tracing

Issues encountered
First we change directory
cd /sys/kernel/debug/tracing
bash: cd: /sys/kernel/debug/tracing: Permission denied

Simple fix of running this in super user mode.
Sudo -s
cd /sys/kernel/debug/tracing

Refered documents
/sys/kernel/debug/tracing/README

How are the typical tracers look like and how to set the tracer

The command cat available_tracers will list out all the tracers avaiable for use.

To set a specific tracer we use echo function_graph > current_tracer to setup the current tracer as function_graph.

In order to check what is the current_tracer set as, we use cat current_tracer.
How to start and stop tracing

We can use echo 0 > tracing_on to disable the tracer and echo 1 > tracing_on to re-enable it.

how to get the trace log and analyse it

We can read a snipbit of the trace using cat trace | head -10
# tracer: function_graph # # CPU DURATION FUNCTION CALLS # | | | | | | | 5) + 19.616 us | } /* do_sched_yield */ 5) + 20.439 us | } /* __ia32_sys_sched_yield */ 5) | syscall_slow_exit_work() { 5) | __audit_syscall_exit() { 5) | path_put() { 5) | dput() {

Analysis of a method load_balance().

 7)               |                    load_balance() {
 7)               |                      find_busiest_group() {
 7)   0.070 us    |                        update_nohz_stats();
 7)   0.080 us    |                        idle_cpu();
 7)   0.070 us    |                        update_nohz_stats();
 7)   0.151 us    |                        idle_cpu();
 7)   3.246 us    |                      }
 7)   4.048 us    |                    }
Link to the kernal’s code
https://github.com/torvalds/linux/blob/24b888d8d59847871387aa3b241b524661070a6e/kernel/sched/fair.c#L8909

Code take from Linux Kernal.
....
group = find_busiest_group(&env);
if (!group) {
schedstat_inc(sd->lb_nobusyg[idle]);
goto out_balanced;
}
.....
We can trace that find_busiest_group() has trigger in the load_balance() function.

TASK
Question 1
a)Ftrace uses memory to keep the trace record. Before starting a	new trace, the old traces are still kept in the memory by ftrace	has to be emptied. How can this be done? (1 mark)

The command echo > trace is used to clear the old traces.

b) What is the command to change the maximum size of the trace	file of ftrace? (1 mark)

The command cat buffer_size_kb shows the size of the current trace
Using the command echo 1408 > buffer_size_kb we can set the trace to the size of your choice.

c)Assuming you are changing the kernel code to insert a printk-	like code to output hello world in ftrace and the message given	by the print code is the only thing you want to trace, show your	code (with comments) and also the tracer that should use in	ftrace. You should provide a shell script that will run the	tracing. (2 marks)

d) Use the function tracer to trace the kernel for about a few seconds. Give the screenshots of the first 20 lines of the trace file and analyse the basic structure of it. (2 marks)

Issues encountered

After installing the kernal I had access to only one tracer.

Inorder to enable function_graph

After installing the kernal

Helping documents:
https://elinux.org/Using_Kernel_Function_Trace

Reference
https://www.cyberciti.biz/tips/compiling-linux-kernel-26.html
https://lwn.net/Articles/365835/
https://lwn.net/Articles/366796/
https://lwn.net/Articles/370423/